## Slide 1
f
Autonomous Vehicle Group
School of ECE
Students Details:
1. D. Shreyas USN:01FE20BEC136
2. Shobith .B USN:01FE20BEC047
3.Prajwal .P USN:01FE20BEC218
4.S.Chandu USN:01FE20BEC328
Guide Details:
Prof. Rohit Kalyani
Project Title: Adaptive Cruise Control
Team No: CIM-A 11

## Slide 2
INTRODUCTION
PROBLEM STATEMENT
SOCIETIAL CONTEXT
NEED STATEMENT
METHODOLOGY
VEHICLE PLATOONING
BIBLIOGRAPHY
Autonomous Vehicle Group
School of ECE
CONTENTS

## Slide 3: DEFINITION
Adaptive cruise control (ACC) is an advanced driver assistance system that automatically adjusts the speed of a vehicle to maintain a safe distance from the vehicle in front of it.
The system uses sensors, such as radar or cameras, to detect the distance and speed of the vehicle ahead, and then adjusts the speed of the vehicle accordingly.
Minor Project- 2023
Autonomous Vehicle Group
School of ECE

## Slide 4: PROBLEM STATEMENT
Develop adaptive cruise control system and evaluate the performance of the system
Minor Project- 2023
Autonomous Vehicle Group
School of ECE

## Slide 5: SOCIETIAL CONTEXT
Improve traffic flow and reduce congestion on roads.
Reduce the frequency and severity of accidents to increase road safety.
Reduce driver fatigue and stress.
Promote sustainable transportation by optimizing vehicle speed and reducing unnecessary fuel consumption.
Improve accessibility for people with disabilities.
Promote responsible driving behaviour.
Improve emergency response times.
Enhance mobility for older adults.
Minor Project- 2023
Autonomous Vehicle Group
School of ECE

## Slide 6: NEED STATEMENT
Need for an advanced adaptive cruise control system that can efficiently adapt to real-world driving conditions, reducing the risk of accidents and improving roadway safety.
Minor Project- 2023
Autonomous Vehicle Group
School of ECE

## Slide 7: METHODOLOGY
Minor Project- 2023
Autonomous Vehicle Group
School of ECE
The Adaptive Cruise Control system will have two modes of steady state operation:
Speed control
Vehicle following (i.e. spacing control)
A standard adaptive cruise control system uses the throttle control input to adjust the vehicle's speed to a desired value. There will be an upper level controller and a lower level controller in the hierarchical longitudinal control system architecture for the cruise control vehicle.
Upper Controller
Lower Controller
Speed set point
Desired acceleration
throttle input
Structure of Speed Control System

## Slide 8
UPPER LEVEL CONTROLLER FOR SPEED CONTROL
A common upper controller algorithm is PI control, which uses speed error as the feedback signal. The mathematical model for controller is given by:
Where, is desired acceleration
is desired velocity
is desired position
Additionally, and are integral and proportional constants respectively.
Mathematical Plant model is given by:
In the model, desired acceleration is given as input and actual velocity is observed at output.
Further, the actual velocity is feed back to calculate the error.
Autonomous Vehicle Group
School of ECE
Minor Project- 2023

## Slide 9
Therefore, we get Transfer functions as:
Hence, The Closed loop System is shown below.
C
P
+
-
Autonomous Vehicle Group
School of ECE
Minor Project- 2023

## Slide 10
SIMPLE LINEAR EQUATION USED FOR VEHICLE FOLLOWING
We have considered a linear equation in which the speed of the vehicle varies linearly with obstacle distance.
Consider two distances stopping distance and nominal tracking distance. We have two speeds at these distances zero speed at stopping distance and nominal set speed at nominal tracking speed.
Taking these conditions into consideration we derive a linear equation which is as follows:
speed_cmd =nominal_speed/(nominal_tracking_distance-stop_distance)*obstacle_distance- nominal_speed/(nominal_tracking_distance-stop_distance)*stop_distance
From this equation speed_cmd varies linearly with respect to obstacle_distance.
Autonomous Vehicle Group
School of ECE
Minor Project- 2023

## Slide 11
Autonomous Vehicle Group
School of ECE
Minor Project- 2023
ADAPTIVE CRUISE CONTROL BLOCK MODELLING
Image processing is done through CSI camera and depth sense camera.
The image processing data is collected for obstacle distance detection and steering command.
The user control block is used to set nominal speed ,nominal tracking distance and stop distance.
This data is further feed to ACC control block for desired speed calculation and speed reduction during turning.

## Slide 12
Autonomous Vehicle Group
School of ECE
Minor Project- 2023
DATA PROCESSING BLOCK
BLOCK DIAGRAM

## Slide 13
Autonomous Vehicle Group
School of ECE
Minor Project- 2023
FLOWCHART

## Slide 14: IMPLEMENTATION DETAILS
SYSTEM ARCHITECTURE
Autonomous Vehicle Group
School of ECE
Minor Project- 2023

## Slide 15: Capture CSI
INPUTS
Data from CSI Camera
OUTPUTS
RGB Image
Autonomous Vehicle Group
School of ECE
Minor Project- 2023

## Slide 16: ColourThresholding HSV
Inputs
RGB Image
Outputs
Binary Image
Autonomous Vehicle Group
School of ECE
Minor Project- 2023

## Slide 17: Region of Interest
INPUTS
Binary Image
ROI
OUTPUTS
ROI Binary Image
Autonomous Vehicle Group
School of ECE
Minor Project- 2023

## Slide 18: LANE LOCATION
INPUTS
Binary Image
Nominal Lane Location
OUTPUTS
Centroid
Steering Command Error
Autonomous Vehicle Group
School of ECE
Minor Project- 2023

## Slide 19: Diagnostics
Inputs
RGB Image
ROI
Binary Image
Nominal Lane Location
Lane Location from Image
OUTPUTS
RGB Image for Display
Autonomous Vehicle Group
School of ECE
Minor Project- 2023

## Slide 20: DEPTH SENSOR
INPUT
RGBD Camera(Intel RealSense)
OUTPUT
RGB Image
Depth Data
Autonomous Vehicle Group
School of ECE
Minor Project- 2023

## Slide 21: OBSTACLE DETECTION
INPUT
Image Depth
Stop Distance
OUTPUT
Image Depth
Distance (m)
Autonomous Vehicle Group
School of ECE
Minor Project- 2023

## Slide 22
Autonomous Vehicle Group
School of ECE
Minor Project- 2023
CONTROL BLOCKS FOR ACC
AUTOMATED DRIVING BLOCK
INPUTS:
obtacleDistance
steering
nominalSpeed
OUTPUTS:
systemCommand
FUNCTIONS:
The input obstacle distance is compared to the nominal tracking distance and stop distance.
If the obstacle distance is smaller than the nominal tracking distance, the nominal set speed will begin to decrease.
When obstacle distance is less than stop distance ,the vehicle speed will scale down to zero.
steering angle calculated using information from image processing.
Accordingly, the desired speed command and steering command is given as output.

## Slide 23
Autonomous Vehicle Group
School of ECE
Minor Project- 2023
TURNING SPEED HANDLING BLOCK
INPUTS:
systemCommand
enable
OUTPUTS:
desiredSpeed
steering
FUNCTIONS:
To ignore the speed reduction during turning set enable to zero
When the enable is set to one, the speed reduction takes place depending upon the sharpness of the turning curve.
If the path is straight line then vehicle travels with nominal set speed.

## Slide 24
Autonomous Vehicle Group
School of ECE
Minor Project- 2023
SPEED CONTROLLER BLOCK
INPUTS:
Arm
DesiredSpeed
measuredSpeed
OUTPUTS:
throttleCmd
FUNCTIONS:
The PI controller tries to obtain the desired speed given as input.
The measured speed is also taken as input for feedforward to map the Desired speed to PWM Duty cycle bias.
Throttle command is then given to the motor.

## Slide 25: BASIC CAR I/0
INPUTS
Motor Command(%,rad)
Indicator Lamps
OUTPUTS
Motor Current(A)
Battery Voltage
Motor Speed(count/s)
Autonomous Vehicle Group
School of ECE
Minor Project- 2023

## Slide 26: TIMING
INPUT
Sample Time
Computation Time
OUTPUT
Timing graph of respective block
Autonomous Vehicle Group
School of ECE
Minor Project- 2023

## Slide 27: INDICATOR AND LAMPS
INPUT
Motor Command
OUTPUT
Indicator and Lamps command
Autonomous Vehicle Group
School of ECE
Minor Project- 2023

## Slide 28: USER CONTROL
INPUT
Arm(1) or Disarm(0)
Speed[0 to 1.5]
OUTPUT
Arm or Disarm
Speed Command
Autonomous Vehicle Group
School of ECE
Minor Project- 2023

## Slide 29: RESULTS
Autonomous Vehicle Group
School of ECE
Desired speed and Actual speed
Graph-1
Minor Project- 2023

## Slide 30
Autonomous Vehicle Group
School of ECE
Fig2. Acceleration v/s Time
Graph-2
Minor Project- 2023
Acceleration(m/s2)

## Slide 31
Autonomous Vehicle Group
School of ECE
Minor Project- 2023
SIGINIFICANCE OF ACC
Fuel Efficiency
One of the significant advantage of ACC is its potential to improve fuel efficiency. By maintaining a constant speed and avoiding sudden braking and accelerating, the system can help reduce fuel consumption, leading to cost savings and environmental benefits.
Convenience
ACC can make driving more convenient and less stressful, especially during long trips. Drivers can relax and enjoy the ride without constantly adjusting their speed to maintain a safe distance from other vehicles.
Safety
ACC can help reduce the risk of collisions by maintaining a safe following distance, even in stop-and-go traffic. This technology can also help prevent accidents caused by human error, such as tailgating, speeding, and distracted driving.
Traffic flow
ACC can also help improve traffic flow by reducing congestion and smoothing out traffic patterns. When more vehicles are equipped with ACC, the overall traffic flow can be more efficient and safer.

## Slide 32: BIBLIOGRAPHY
W. Pananurak, S. Thanok and M. Parnichkun, "Adaptive cruise control for an intelligent vehicle," 2008 IEEE International Conference on Robotics and Biomimetics, Bangkok, Thailand, 2009, pp. 1794-1799, doi: 10.1109/ROBIO.2009.4913274.
A. Abdullahi and S. Akkaya, "Adaptive Cruise Control: A Model Reference Adaptive Control Approach," 2020 24th International Conference on System Theory, Control and Computing (ICSTCC), Sinaia, Romania, 2020, pp. 904-908, doi: 10.1109/ICSTCC50638.2020.9259641.
X. Zhang, W. Li, K. Guo, T. Peng and Y. Huang, "Longitudinal acceleration allocation for cooperative adaptive cruise control including platoon kinematics," 2019 IEEE 28th International Symposium on Industrial Electronics (ISIE), Vancouver, BC, Canada, 2019, pp. 1512-1517, doi: 10.1109/ISIE.2019.8781428.
Autonomous Vehicle Group
School of ECE
Minor Project- 2023

## Slide 33: THANK YOU
Autonomous Vehicle Group
School of ECE